## Slide 1: Zenbo Caretaker
Ms. Chidchanok Bunjongpean
Mr. Krittamet Kiattikulwattana
Mr. Teekavu Sucharitakul
Ms. Vipawan Jarukitpipat
Network Computing Laboratory
Professor Chih-Lin Hu
Faculty of Information and Communication Technology
Mahidol University

## Slide 2
Introduction

## Slide 3: Outline
System Overview
  System design
  Protocol
Development
Testing & Result
Conclusion & Suggestion
Future Plan

## Slide 4: Project Detail
Group Users
Elderly
Family Members
Purpose
To reduce the cost of elder care
To fill the gap between the number of available caregivers and the aging population.
To allow users to easily control the home appliances
To enhance better home experience for the users

## Slide 5: System Overview
1

## Slide 6
Caretaker Service
Safety
Home Automation
Behavior Recognition
Control Home Appliances
Environment Sensing
Services
Fall Detection
Smoke & Fire Detection
Module
Routine
Diet
Medicine
Lights
Temperature
Humidity
Software
Engineering
- Image Processing
-Machine Learning
- Sync data from wearable
- Raspberry Pi
- Node - RED
- Sensors
- Image Recognition
Overall system

## Slide 7: System Design

## Slide 8: Scope
Zenbo & Android Application
Node - RED & Raspberry Pi
Home Appliances Controlling System

## Slide 9: System Flow Overview
3. Analyse and classify command
1. Detect and display
user command
4. Activate the sensors and obtain data
5. Generate the response
6. Send the response back to Zenbo
7. Display response on the screen
2. Send the command to Node - RED

## Slide 10: Scenario
Interaction
Control
Update
Control
Control

## Slide 11: Use Case
Zenbo
Raspberry Pi
Users

## Slide 12: Tools
Programming Language
Editor
API
Javascript (Node JS)
Java
Android Studio
Node - RED
Android
Speech Recognition
Zenbo
Zenbo SDK
Library
Android
OKHttp

## Slide 13: Flow

## Slide 14: Protocol

## Slide 15: Voice Command Protocol
3 main components
The order doesn’t matter
<Operation> <Room> <Sensor’s name / Appliances>
Turn on Bedroom Tesla
Turn on Bedroom light

## Slide 16
Room | Sensor name’s | Appliances | Command
Bedroom | Tesla | Light | Turn on Bedroom Light Turn on Bedroom Tesla
 |  |  | Turn off Bedroom Light Turn off Bedroom Tesla
 | Elsa | Air Conditioner | Turn on Bedroom Air Conditioner Turn on Bedroom Elsa
 |  |  | Switch Bedroom Air Conditioner to dry/cool mode Switch Bedroom Elsa to dry/cool mode
 |  |  | Increase / Decrease Bedroom Air Conditioner Temperature Increase / Decrease Bedroom Elsa Temperature

## Slide 17
Room | Sensor name’s | Appliances | Command
Bedroom | Gray | Temperature and Humidity Sensor (DHT22) | Bedroom Temperature Sensor Bedroom Temperature Gray
 |  |  | Bedroom Humidity Sensor Bedroom Humidity Gray

## Slide 18
Room | Sensor name’s | Appliances | Command
Living room | Tim | Light | Turn on Bedroom Light Turn on Bedroom Tesla
 |  |  | Turn off Bedroom Light Turn off Bedroom Tesla
 | Dan | Television | Turn on Living room Television Turn on Living room Dan
 |  |  | Turn off Living room Television Turn off Living room Dan
 |  |  | Change Living room Television to next channel
 |  |  | Change Living room Television to previous channel

## Slide 19: Development
2

## Slide 20: Zenbo and Android Application

## Slide 21: Develop Android Application

## Slide 22: Android Application Demonstration

## Slide 23: Testing and Result
3

## Slide 24: Test
Zenbo
Zenbo is able to receive voice command
Command successfully sent to Node - RED via Http GET
Application receives and displays the response
The Button is able to use and open Node - RED dashboard on the browser
Raspberry PI
Node - RED receives the command
Node - RED can correctly classify the command and generate response according to command condition
Node - RED can read the data and control the sensors

## Slide 25: Video Demonstration
Notes: ใส่ Subtitle
ชี้ใน Clip Video ว่าทำอะไรอยู่
ตอนนี้เราสั่งคำสั่งอะไร
มีทั้งภาพและตัวอักษรอธิบาย

## Slide 26: Conclusion and Suggestion
4

## Slide 27: Conclusion
Zenbo is able to receive, display voice command and send the text command to Node-RED.
Node-RED is able to receive and interpret the command, update values, and control home appliances.
The voice recognition is not able to detect the correct command when the command is too complex or hard to pronounce which result in invalid command

## Slide 28: Future Plan
5

## Slide 29: Future Plan
Move the command analysis function from Node - RED to Android application on Zenbo
Integrate Face or Voice recognition system to identify the users
Implement the system that is able to recognize users habits and suggest home configuration preference.
Support other existing IoT devices
Example of Face Identification using Microsoft Face API
Able to open an application on Zenbo using Voice command

## Slide 30
Thank you

## Slide 31
Q&A
Notes: Name using device where
Add ห้องที่ไหน
This is only prototype
Use LED light represent home appliances:
อย่าปล่อยให้ Presentation เงียบ

## Slide 32: June
 | 1 Jun - 9 Jun | 10 Jun - 16 Jun | 17 Jun - 23 Jun | 24 Jun - 30 Jun
Seminars |  |  |  | 
RPi installation |  |  |  | 
RPi Sensors |  |  |  | 
RPi Camera |  |  |  | 
IoT Communication Protocol |  |  |  | 

## Slide 33: July
 | 1 Jul - 7 Jul | 8 Jul - 14 Jul | 15 Jul - 21 Jul | 22 Jul - 27 Jul
Research on Zenbo and Node - RED |  |  |  | 
Node - RED |  |  |  | 
Android Application |  |  |  | 
Android Voice Recognition |  |  |  | 
Android OKHttp |  |  |  | 
Prepare Presentation |  |  |  |